## Slide 1: Electrical Risks, Safety and Solutions for Older Homes
Presented by:
Brian Cook
PowerCheck Electrical Safety Services
www.powercheck.ca
Notes: <number>

## Slide 2: BC Fire Statistics
Reported fires per year
  Reported fires: 4500–6000
  Fire fatalities: 18–32
Electrical fires:
  186 (5 year average)
  Represents about 10% of residential fires
In about 40% of reported fires the cause of fire is unknown. Electrical may have been the cause.
© PowerCheck Electrical Safety Services 2012
Notes: <number>

## Slide 3: Old house: Higher probability of fire
In 25%, house construction date unknown. Data source: BC OFC
© PowerCheck Electrical Safety Services 2012

## Slide 4: What is causing the electrical fires?
Original wiring
  Important to check, sometimes faulty
  Not the leading cause of fire
Handyman tinkering
  Accounts for the vast majority of electrical fires.
  Probability of handyman tinkering present increases with age of home
  Old houses often found rampant with “Hazardous handyman add-ons”!
Hazardous add-ons are common in older houses. These dangerous additions put the house at high risk of electrical fire.
© PowerCheck Electrical Safety Services 2012
Notes: <number>

## Slide 5: Electrical System Components
Three components to your electrical system:
  Service & Panelboard
  Wiring
  Electrical devices
    (switches, receptacles, lights)
Service & Panelboard
Wiring
Electrical devices
© PowerCheck Electrical Safety Services 2012

## Slide 6: Service size: 100 amps or 60?
Until the1970s, 60 amp service was the norm in single-family homes
If there has been no additional circuits: Original 60 amp service is still acceptable and safe today
60-amp service is often not recognized.
Enclosure is rated for 100 amps but inside box is 60 amp service
60-amp fuses, 60-amp service
“Rated for 100 amps”
© PowerCheck Electrical Safety Services 2012
Notes: <number>

## Slide 7: Main circuit breaker can present incorrect service size
These illegal upgrades present what appears to be 100 & 200 amp services, but in fact both are very hazardous 60 amp services (Note the wire size: 60 amps).
200 amp
60 amp
© PowerCheck Electrical Safety Services 2012

## Slide 8: Common hazard in panelboards: Overrated circuit breakers
15 amp circuit breaker
30 amp circuit breaker
© PowerCheck Electrical Safety Services 2012
Notes: <number>

## Slide 9: Overrated circuit breakers can result in over-heated conductors
© PowerCheck Electrical Safety Services 2012
The circuit breaker provides the protection of the wires from overcurrent. If the circuit breaker is oversized, it won’t trip when needed
Notes: <number>

## Slide 10: Wiring before 1950
Knob-and-tube. The standard in homes before 1950.
If outlets have been changed, and basement enclosed, knob-&-tube often not identified.
Knob-&-tube: Still present in most pre-1950 homes today.
Original two-prong, ungrounded receptacle. Prior to 1950 this would have been fed by knob-and-tube conductors
© PowerCheck Electrical Safety Services 2012
Notes: <number>

## Slide 11: Knob and tube: Qualities
A well designed system:
  Heavy gauge conductors
  Spaced well apart
  Soldered connections
Work seldom done by non-professionals
Knob and tube wiring runs along the studs and through the joists of older homes.
knobs
tubes
© PowerCheck Electrical Safety Services 2012
Notes: <number>

## Slide 12: Knob and tube: Hazards
No ground protection
Not suitable for high-temperature lighting
Handyman add-ons
Original 2-prong outlet swapped for modern 3-prong, falsely presenting receptacle is grounded.
© PowerCheck Electrical Safety Services 2012
Notes: <number>

## Slide 13: Knob and tube: Solutions
Rewire: $20,000 + or
The wiring usually checks out fine: Therefore GFCIs provide excellent ground protection: $20 each
AN EXCELLENT & SAFE SOLUTION!
GFCI receptacle provides excellent ground protection.
© PowerCheck Electrical Safety Services 2012
Notes: <number>

## Slide 14: Knob and tube findings
In 99% of homes:
Knob and tube wiring is still in homes today
  Usually not visible due to new panel and finished basement.
Knob-and-tube wiring is in excellent condition
  No need for expensive replacement, but:
Original 2-prong outlets now modern 3-prong
  Falsely presenting outlets are grounded, thus rated “High Risk”
  Cost to eliminate fire risk of knob-&-tube: Less than $500
RESULT: SAFE AND HAPPY HOMEOWNERS!
© PowerCheck Electrical Safety Services 2012
Notes: <number>

## Slide 15: Wiring of the 1950s
Ungrounded wiring continued through the 1950s.
Same concerns as knob-&-tube
Requires GFCIs for ground protection
Ungrounded 2-prong receptacle fed by “modern” cable, NMD1
© PowerCheck Electrical Safety Services 2012
Notes: <number>

## Slide 16: Wiring of the 1960s
Grounding of receptacles: 1962
New cable introduced with ground
Insulation still not suitable for high-temperature lighting
New cable of the 1960s “NMD3 with ground”.
© PowerCheck Electrical Safety Services 2012
Notes: <number>

## Slide 17: Wiring of the 1970s
Modern electrical cable introduced, suitable for recessed lighting.
Hazardous wiring abounds!!:
  Due to the rapid rise in basement suites, kitchen renos & powering of garages: Unauthorized electrical work thrives.
  This is encouraged with the proliferation of self-help books and easy access of electrical supplies.
Modern cables: NMD7 & NMD90 But along with it comes “do-it-yourselfers”.
© PowerCheck Electrical Safety Services 2012
Notes: <number>

## Slide 18: The Aluminum Years: 1966–1974
Aluminum wiring: A cost-effective solution due to the high price of copper 1966–1974
Installed in the vast majority of homes during that period
Still present today in nearly all of these homes
An aluminum-rated receptacle for use with aluminum wiring.
© PowerCheck Electrical Safety Services 2012
Notes: <number>

## Slide 19: The Aluminum wiring fire hazard
Original system fine however
Original outlets and switches swapped for modern outlets and switches not rated for aluminum
Original aluminum-rated outlets are commonly found swapped for modern, non-aluminum-rated outlets.
© PowerCheck Electrical Safety Services 2012
Notes: <number>

## Slide 20: The Aluminum wiring solution
Rewire: $20,000 + or
Approved copper pigtailing (or aluminum rated devices) Typical cost: $1000 - $1500
NOTE: “Approved” means with the correct wire connectors
Aluminum-wiring pigtailing with incorrect wire connectors; commonly found.
© PowerCheck Electrical Safety Services 2012
Notes: <number>

## Slide 21: Hazardous add-ons Abundant in older houses!
Undersized cables
Incorrect cables
Ungrounded cables
Oversized circuit breakers
Bad electrical connections
“Mouse holes”
BX cables incorrectly installed
All these deficiencies create Real fire hazards!
© PowerCheck Electrical Safety Services 2012

## Slide 22: Hazardous add-ons Exposed electrical connections
© PowerCheck Electrical Safety Services 2012
Exposed connections
If connections become at all loose they will arc, easily igniting surrounding wall material.
Common
Notes: <number>

## Slide 23: Hazardous add-ons No junction box behind lampholder
© PowerCheck Electrical Safety Services 2012
If connections become at all loose they will arc, easily igniting surrounding ceiling material.
Common
Notes: <number>

## Slide 24: Hazardous add-ons Extension cords stapled to walls
© PowerCheck Electrical Safety Services 2012
staples
Staples put pressure on cord. Over time the cord insulation breaks down. The staple then creates a direct short across the wires, which can easily result in fire.
Common
Notes: <number>

## Slide 25: Hazardous add-ons Baseboard heaters incorrectly installed
© PowerCheck Electrical Safety Services 2012
“Seven firefighters said the fire began about 1 a.m. near an electric baseboard heater. Three children died, ages 6, 2 and 14 months” (Cleveland News, Dec 5, 2007).
Incorrect installation can easily result in electrical fires.
Notes: <number>
http://blog.cleveland.com/metro/2007/12/third_child_killed_by_shaker_h.html

## Slide 26: Inadvertent actions can create fire hazards
Copper water pipe repairs with “PEX” can disconnect the grounding
Old hot-water-tank cable, live and dangling; often near the gas line.
These deficiencies create Real fire hazards!
© PowerCheck Electrical Safety Services 2012

## Slide 27: Summary
© PowerCheck Electrical Safety Services 2012
Electrical fire hazards in most homes built before 1975.
Though deterioration of older wiring is occasionally found, the vast majority of fire hazards are due to handyman tinkering.
Notes: <number>

## Slide 28: A solution for safety: An electrical examination
An electrical examination finds out what needs to be done to make house safe!
© PowerCheck Electrical Safety Services 2009

## Slide 29: The PowerCheck examination
© PowerCheck Electrical Safety Services 2012
Comprehensive
Conducted by master electrician (FSR in BC)
Third party examination only
Notes: <number>

## Slide 30: The result
© PowerCheck Electrical Safety Services 2012
Safe houses
Happy homeowners
Over 4000 clients have had their electrical system examined by PowerCheck. Nearly all have said, “It was the best thing that we have ever done”.
Notes: <number>